## Slide 1
Presentation on
Coastal Vulnerability using Remote Sensing and GIS
OTGA-INCOIS Training Course on "Coastal Vulnerability Mapping and analysis using QGIS" during November 25-29, 2024.
Organized by International Training Centre for Operational Oceanography (ITCOocean) ESSO-INCOIS, Hyderabad, India
By
Dr. R S Mahendra
Scientist ‘F’, ARO Division,
mahendra@incois.gov.in

## Slide 2: Impact of climate change on the Indian Ocean
(a) Time series of global heat content anomaly for the 0-700 m (in 1022 Joules). (b) for Indian Ocean. (c) Spatial heat content anomaly (0-700 m) for Indian Ocean (1022 J/decade)
MoES Climate Assessment Report
SST trend (oC/decade) from: (a) observed Extended Reconstructed Sea Surface Temperature, version 4 (ERSST v4) during 1951– 2015, (b) CMIP5 historical simulations for 1976–2005.
Notes: Added detail in the caption of the left side figure. Modified references by including journal name.

## Slide 3: Where Does the Heat Go?
Source: Cazenave et al 2018
Source: Laury Miller, NOAA Lab for Satellite Altimetry

## Slide 4: Sea Level Rise in the Indian Ocean
(Top) Sea level trend during the altimeter duration show large spatial variability across the globe. In the tropics, the maximum sea level rise of more than 5 mm/yr is observed in the western Pacific, south tropical Indian Ocean and in the northern Bay of Bengal.
150 mm
100 mm
150 mm
300 mm
Mumbai
Kochi
Vizag
Kolkata
Relative Sea level change based on the tide gauges located along the west and east coast of India suggest a 10-30 cm of sea level rise during the period of 1950-2015.
Notes: Added detail in the caption of the left side figure. Modified references by including journal name.

## Slide 5: Current Rate Nearly Twice the 20th Century Rate Largely Due to Volume Changes
Volume
Mass
Volume
Total
Mass
Total
1920 - 1990 1992 - 2003
0.5 mm/yr
1.8 mm/yr
1.3 mm/yr
1.5 mm/yr
1.7 mm/yr
3.2 mm/yr
Source: Laury Miller, NOAA Lab for Satellite Altimetry
Sea Level Budget Changes With Time

## Slide 6
Sea-level rise Global Scenario
Source: 5th IPCC report
Representative Concentration Pathways (RPCs) 6.0
Average global sea level rise 1.8 mm/y
Green House Gas (GHG) emissions (measured in CO2 – equivalent)
RCP | Criteria | Radiative Forcing (W/sq m) | Mean rise (cm) | Range (cm)
4.5 | GHG emissions peaks around 2040 then decline | 4.5 | 53 | 36-71
6.0 | GHG emissions peaks around 2080 then decline | 6.0 | 55 | 38-73
8.5 | GHG emissions continue to rise throughout | 8.5 | 74 | 52-98

## Slide 7: Altimeter Record of Sea Level Rise Over Past 15 Years

## Slide 8
Indian ocean sea level Observations (Altimeter)
Notes: Region wise increasing trend of sea level of INDIAN OCEAN(x=30E:120E,y=30S:30N), NORTH INDIAN OCEAN(x=40E:100E,y=0:30N), ARABIAN SEA(x=50E:78,y=8N:26N) and BAY OF BENGAL (x=77E:103E,y=5N:23N). All regions especially NIO are characterized by sharp rise in the increase trend of sea level for the period-II (2004-2013) relative to the previous period-I (1993-2003).
Source: Altimeter

## Slide 9
Sea-level rise Indian Scenario
Mean sea-level-rise trends along the Indian coasts are about 1.30 mm/yr based on past tide gauge records. Even with the same rate expected SLR of about 13 cm by 2100
Diamond Harbour | 5.04
SLC=5.04mm/y
SLC=0.74mm/y

## Slide 10
Implications of climate change and sea level rise

## Slide 11: Importance of Oceans and Coasts
Our Planet Earth
  70% Oceans
  20% Coasts
The Coasts
A Fragile Coastal Ecosystem with a Large Community around
High biological productivity (14 %), wealth of species and genetic diversity (90 %) and fluvial discharge (75-90 %).
High rates of population growth, development of industries, trade and commerce (60 % of human population, 2/3 of the world’s large cities)
Degradation of ecosystems, diminishing living resources and deteriorating water quality.
Episodic events, cyclones, floods, tsunami, etc.
Impact on climate.
The Oceans
A Vital Source for Resources
A Driving Force for Monsoons
A Realm for Cyclo-genesis
A Medium for Transport
A Strategic Space

## Slide 12
Dynamical Oceanic Processes
Ocean Circulation
Tides
Fronts
Up-welling
Mixed Layer Dynamics
Waves
Biological processes
Productivity
Biota
SST
Sea Level
Bottom Topography
Chemical Processes
Salinity
Nutrients
Co2 sink
Physical
processes
Coastal / Estuarine Dynamics
Coastal
topography

## Slide 13
SST
Radiometer
(VIS-TIR)
Ocean Colour
Coastal Process
Coastal land use
Radiometer
(VIS, NIR)
Wind Speed
SST
Sea Ice Extent
Radiometer
(MW)
Wave Ht.
Sea Level
Sea Ice
Elevation
Altimeter
Surface Wind
Vector
Scatterometer
Wave Spectrum
Sediment
Oil spill
SAR
Remote Sensing Observations
Role of RS in Coastal Management
Development of accurate, up-to-date and comprehensive scientific data base.
Coastal & Ocean Information Services
Inventory on habitats, landforms, shoreline, land use, exploration of fisheries, mitigation of disasters, understanding sediment dynamics, etc.
Provide Inputs for making decisions on construction setback lines, site selections, risk analysis, ecosystem modelling, etc.
IRS
Oceansat-1, 2 & 3

## Slide 14
Modeling/Research
Ocean Information/ Advisory services
Multi mode Dissemination
Real time observations
STAKEHOLDERS OF BLUE ECONOMY
Customized products
Hazard based products
Fisheries & Ecosystem services
Ocean Information System for blue economy

## Slide 15
Argo, Moorings, ADCP, drifters, RAMA buoys, current meter moorings, XBT, CODAR, Tsunami buoys, wave rider buoys
In-situ Observation Systems by India

## Slide 16
  Global forecast (Wave watch III)
  Regional forecast (Mike wave and ROMS general circulation)
    Sea Surface Currents; Sea Surface Temperature; Mixed Layer Depth; D20
    Significant Wave Height; Swell Wave Height; Wave Periods; Swell Wave Periods; Wind Speed
  Coastal forecast (Waves; Mike; 10 KM; 7 day ; 3 hourly)
  Location specific forecast (Waves; Mike; 5 KM)
    Pondicherry; Tuticorin; Tirunelveli; Vizag; Ratnagiri; Karwar
  Value added services
  High wave alerts
Ocean Modelling

## Slide 17
More than 50 Nations around
Many are Developing Countries
Most of the coastal areas are low lying and vulnerable to oceanogenic disasters such as Tsunamis, Storm Surges, Sea-level rise
Frequent Cyclones - 13% of World’s cyclones in the Seas around India
A few Tsunami events in the past - Dec 26, 2004 Tsunami resulted in a loss of 18,045 deaths and 6,47,599 persons displaced
More than1.5 Billion Population
More than 66,500 km coastline
250 million live within 50 km of the coast
3,600 fishing villages
12 major ports and 185 minor ports
4,120 sq km of mangroves
Vulnerability of the Indian Ocean Coastline to Oceanogenic Disasters
Shoreline erosion and hazardous storms greatly affect coastal environment quality (edaphic), limiting agriculture land use and its mitigation.
Flooding and Salinity Many coastal agricultural areas are fat, while others have steep coastlines. Low-lying agricultural land is frequently subjected to severe drainage and soil salinity problems due to stagnation of rain and runoff water and fooding from rivers or periodic storm surges

## Slide 18
13% of World’s cyclones
in the Seas around India
Annual; Frequent phenomenon
Inundation of Coastal areas
Oceanogenic Disasters
Tsunami in Indian Ocean
A few events in the past
Inundation of Coastal areas (Large stretches)
Highly devastative Tsunami on
Dec 26, 2004
Tsunami, Cyclones, Storm surge, Sea level rise, Coastal erosion, High Waves, etc.
Coastal
Inundation
Damage

## Slide 19
Characteristics of, and responses to, marine physical hazards
Source: UNESCO/IOC Report on Coastal Vulnerability

## Slide 20
Vulnerability and Role of Geospatial Technology
2018 Humanitarian Needs Overview (HNO)
  Vulnerability is the degree to which a system is prone to harmful effects of climate change and its variability and extremes (IPCC 2001). Vulnerability is a function of hazard, exposure and sensitivity of physical or biophysical components.
  Approach: Deterministic and Probabilistic
Geospatial Technology plays a vital role in the disaster management cycle for information and informed decisions
Potential Impact
Sensitivity
Exposure
Adaptive Capacity
Vulnerability

## Slide 21
Coastal Vulnerability Mapping
Tsunami Hazard Vulnerability
Storm Surge vulnerability
Shoreline Change
CVI
MHVM
3D GIS
Socioeconomic Vulnerability

## Slide 22
ALTM data for the coasts between Paradeep- Kochi
Carto-DTM for the Indian Mainland.
RTK-GPS data collected in some areas using GPS
Bathymetry data available from all the sources
Base Data Used
Parameters | Source | Longitude | Latitude | Magnitude
Sumatra 2004 | Sumatra | 95.850 E | 3.320 N | 9.3 Mw
Car Nicobar 1881 | Car Nicobar | 92.43 | 8.52 | 7.9 Mw
Andaman 1941 | North Andaman | 92.50 E | 12.10 N | 7.7 Mw
Marakan 1762 | Arakan | 94 | 19 | 8.8 Mw
Worst-Case | Car Nicobar | 92.43 | 8.52 | 9.3 Mw
Worst-Case | North Andaman | 92.43 | 8.52 | 9.3 Mw
Historical & Worst case scenario
Topography and Bathymetry Data
Tsunami Inundation modeling and vulnerability mapping
Notes: Input data used for the modelling and the source of historical tsunami considered

## Slide 23
1:25000
1:5000
Vulnerability classification
Low risk – Carnicobar Eq (8.1.Mw)
High risk – Sumatra Eq (9.3Mw)
Maximum risk – Hypo. Carnicobar Eq (9.3 Mw)
II. Inundation Depth
water level due to Sumatra 2004
III. Others details
From Satellite Imagery
  Landuse
From DC images (upto 2 km from coast)
  Elevation Contours
  Infrastructure details
  Trees
  Roads
  Railways
  Buildings
Secondary data
  Cadastral boundaries and Survey Nos
  Administrative boundaries
Mapping of Coastal Vulnerability to Tsunamis
Notes: 23

## Slide 24
Storm Surge Early Warning
Cyclone track
Rushikulya river
Customized and configured ADCIRC model for the Indian Ocean domain.
Blended parametric and global model winds.
Probabilistic Storm Surge (P-Surge) estimation.

## Slide 25
Mapping of Coastal Vulnerability to storm surge

## Slide 26
Shoreline Change Studies ...
Shoreline change in Lakshadweep Islands
Satellite data gives useful insights in assessing the long term shoreline changes
GIS analysis helps in understanding the spatio-temporal dynamics
The integration of the relevant information will enable us to understand possible cause
Plan for the remedial measures
The technology also useful in understanding the future implications

## Slide 27
Impact of Coastal Structures on the shoreline
The construction of breakwater structures disturbs the natural coastal processes
As the net drifts is towards the north in this region, northern parts observed increased erosion due to a lack of sediments for the natural coastal currents.
Shoreline Change Studies ...

## Slide 28
Parameter | Data
Geomorphology | IRS LISS-IV
Slope | GEBCO
Elevation | SRTM
Tidal Range | Astronomical tide from WXTide-32
Shoreline Change Rate | Landsat data (1972-2000)
Historical Sea Level | GLOSS long term tide gauge observation
Significant Wave Height | Simulated data from Mike model
Data Used
Coastal Geomorphology
Coastal Regional Elevations
Coastal Slope
Shoreline-change Rate
Methodology
Input Parameters
Geological
Sea-level-change Rate
Mean Significant Wave Height
Tide Range
Tsunami Run-up
CVI Maps
Output
Coastal Vulnerability Atlas
Risk Rating
Analysis
Where
  a = Shoreline change rate (m/y)
  b = Sea level change rate (mm/y)
  c = Coastal slope (degree)
  d = Significant wave height (m)
  e = Tide range (m)
  f = Coastal regional elevation (m)
  g = Coastal geomorphology
CVI = √ [(a*b*c*d*e*f*g)/7]
Physical
Assessment of Coastal Vulnerability Indices (CVI)

## Slide 29
  CVI Atlas covering Indian coast comprising 156 maps on 1:1lakh scales has been prepared and released on May 09, 2012
INCOIS, (2012). Coastal Vulnerability Atlas of India. INCOIS-ASG-CGAM-CV-2012-01, Pages 212, Maps 156, INCOIS, Hyderabad, India. ISBN 978-81-923474-0-0.
Atlas Released
on 10/05/2012
Coastal Vulnerability Atlas

## Slide 30
20m
5m
10m
Coastline in 1950
Coastline in 2005
Predicted erosion in 100 yrs
Predicted 100 year flood level
Composite 100 year hazard line
Coastal Multi-hazard Vulnerability Assessment
“The Multi-Hazard Map is a “composite, synthesized and overlay of multiple hazards”

## Slide 31: Data and Parameters
Data | Resolution (m) | Period | Parameters
ALTM | 5 | 2007 | Elevation Contours
Carto DTM | 10 | 2006-07 | 
Landsat, MSS | 57 | 1972 | Shoreline Change
Landsat, TM | 30 | 1990 | 
Landsat, ETM | 30 | 2000 | 
Tide gauge | -- | 1952-2005 | Sea Level Change
Hourly Tide gauge data and Published sources |  |  | Extreme Water Levels

## Slide 32
High Altitude
Low Altitude
Very Low Altitude
Terrestrial
IKONOS Cartosat
Quickbird
Worldview
Etc.
Examples of 3D Mapping Techniques

## Slide 33
The SLRP-2 has been used to calculate the predicted data to estimate the residuals
Extreme Water level return period was estimated for the above stations based on the Grigorton probability distribution method
Assessment of extreme water level from historical tide data
Chart: 
| 38877.916666666664 | 38877.958333333343 | 38878 | 38878.041666666584 | 38878.083333333336 | 38878.124999999993 | 38878.166666666584 | 38878.208333333336 | 38878.25 | 38878.291666666388 | 38878.333333333336 | 38878.375 | 38878.416666666664 | 38878.458333333343 | 38878.5 | 38878.541666666584 | 38878.583333333336 | 38878.624999999993 | 38878.666666666584 | 38878.708333333336 | 38878.75 | 38878.791666666388 | 38878.833333333336
Obs | 0.37 | 0.22 | 0.09 | 0.09 | 0.17 | 0.33 | 0.53 | 0.75 | 0.89 | 1.04 | 4 | 0.91 | 0.71 | 0.53 | 0.37 | 0.29 | 0.25 | 0.33 | 0.47 | 0.61 | 0.73 | 0.8 | 0.76
Prd | 0.51183 | 0.3392 | 0.22865 | 0.20902 | 0.28467 | 0.44282 | 0.65036 | 0.8592 | 1.0232 | 1.1076 | 1.0934 | 0.98481 | 0.81286 | 0.62836 | 0.48252 | 0.40557 | 0.40575 | 0.47945 | 0.60839 | 0.75568 | 0.87686 | 0.93448 | 0.90739
res | -0.14183 | -0.1192 | -0.13865 | -0.11902 | -0.11467 | -0.11282 | -0.12036 | -0.1092 | -0.13324 | -0.067615 | 2.9066 | -0.074805 | -0.10286 | -0.09836 | -0.11252 | -0.11557 | -0.15575 | -0.14945 | -0.13839 | -0.14568 | -0.14686 | -0.13448 | -0.14739
Probability of non-exceedence
Where,
‘m’ is rank of the variable (Water level)
‘N’ is the total number of observations
Return Period
Where,
‘U’ is the extreme water level
‘R’ is the return period in years,
‘a’ is the slope (fig.A)
'u’ is the intercept (fig.A)
A
B

## Slide 34
Composite Multi-hazard line
High Resolution Topography
Extreme Water Level and return periods
Shoreline Change Rate
Composite Multi-hazard Line
Coastal Multi-hazard Vulnerability Assessment
Sea-level Change Rate
INPUTS
OUTPUTS
SYNTHESYZED SPATIAL OVERLAY ANALYSIS
Multi-hazard Vulnerability Map
Notes: Process of generation of the MHVM

## Slide 35
Composite Multi-hazard Line
0
8.0
Meters
Composite Multi-hazard line

## Slide 36
Multi-hazard Zones
Hazard Zone
Safe Zone

## Slide 37
Landuse/Landcover

## Slide 38
Roads
Vannara Palyam Road
Beach Road
Mettu Street
Peliyar Kovil Street
Beach Road
Kovil Teru Street
Major
Minor
Streets
Roads

## Slide 39
Buildings
Buildings

## Slide 40
Hazard Zone
Safe Zone
Layer Integration
Major
Minor
Streets
Roads
Hazard
Safe
Buildings

## Slide 41
Coastal Geospatial Applications Mission, ASG
Risk
High
Moderate
Low
No Risk
Risk Map

## Slide 42
Hazard
Safe
Buildings
Risk
High
Moderate
Low
No Risk
Streets
Evacuation
Routs
Major
Minor
Roads
Hazard Management

## Slide 43
3DVAS
3D GIS Mapping
MHVM
High Vulnerable Areas
High Vulnerable Areas
Kakinada
Machilipatnam
Nizampatnam-Vatapalem
Chennai
Cuddalore-Pondicherry
Tuticorin
Alleppey- Chevara
Rameshwaram
Puri
3D Buildings of Machilipatnam
3D Buildings of Machilipatnam
3D Buildings of Pondicherry
3D Buildings with Socio-economic data of Pondicherry
3D Buildings with Socio-economic data
Of Machilipatnam

## Slide 44
Coastal Risk Assessment at Building level
3m
2m
1m
Inundation
Depth
Socio-Economic Risk for Tsunami
Very High
Moderate
High
Low
Building Risk
Very High
Moderate
High
Low
Building Risk
Very High
Moderate
High
Low
Building Risk

## Slide 45
Model setup, propagation and inundating modeling,
Overlay of the modeling results and risk assessment at building level and generation of outputs
Inundation Modelling and risk assessment in 3DVAS

## Slide 46
MHVM risk assessment up to village level
Mahendra et al., 2021

## Slide 47
Socio-Economic Vulnerability Index case study1
Sensitivity (social)
(1) Small and marginal farm(ers) (SMF)
(2) Agriculture labourers (AL)
(3) Fishers population (FP)
(4) Malnutrition (FSM)
(5) Population density (PD)
(6) SC/ST population (SCST)
Sensitivity (economic)
(7) Net sown area (NSA)
(8) Annual rainfall (AR)
(9) Dependence on natural resource (DNR)
(10) Distance to nearest town (DNT)
(11) Distance to nearest hospital (DNH)
Adaptive capacity (social)
(1) Education status (ES)
(2) Household amenities (HA)
(3) Housing condition (HC)
(4) Community infrastructure (CI)
(5) Population growth rate (PGR)
(6) Gender ratio (GR)
Adaptive capacity (economic)
(7) Transport and communication (TC)
(8) Economic dependency ratio (EDR)
(9) Access to market (AM)
(10) Net irrigated area (NIA)
(11) Groundwater development (GD)
(12) Livestock population (LP)

## Slide 48
Socio-Economic Vulnerability Index case study2
54 indicator parameters

## Slide 49
Socio-Economic Vulnerability Index case study3
SEVI=SI/1+ACI
CVI
Index Category | Parameters
Exposure Index | MHVM Zones
 | Elevation
Sensitivity (Social) | Marginal workers
 | Population Density
 | SC/ST percentage
Sensitivity (Economic) | Annual Rainfall
 | Distance to Nearest Town
 | Distance to Nearest Hospital
 | Non-worker Percentage
 | The average size of households
Adaptive capacity (social) | Sex Ratio
 | Literacy Rate
 | Average Cultivable land per Household
 | Work Participation Rate
Adaptive capacity (Economic) | Net Irrigated area
 | Transport Facility
 | Banking Facility
Mahendra et al., 2023

## Slide 50
Terry P. Hughes et al. Science 2018;359:80-83
(A) Number of 100 pantropical locations that have bleached each year from 1980 to 2016. Black bars indicate severe bleaching affecting >30% of corals, and white bars depict moderate bleaching of <30% of corals.
(B) Cumulative number of severe and total bleaching events since 1980 (red; right axis) and the depletion of locations that remain free of any bleaching or severe bleaching over time (blue; left axis).
(C) Frequency distribution of the number of severe (black) and total bleaching events (red) per location. (D) Frequency distribution of return times (number of years) between successive severe bleaching events from 1980 to 1999 (white bars) and 2000 to 2016 (black bars).
Temporal patterns of recurrent coral bleaching.
Notes: Slide showing the increased frequency of coral bleaching globally

## Slide 51
Chart: Date (ddmmmyy)
Coral Bleaching Alert System (CBAS) - A satellite derived SST based Service
Coral Bleaching
Threshold
Recent bleaching event was recorded during the April-May 2016 at Andaman validated with Field Data
“Satellite based advisory service to predict thermal stress on an important coral ecosystem”
Methodology
Service initiated since Feb 2011 and 122 advisories provided every year

## Slide 52
Tobita, et al, 2005
Tectonic disturbances
Total Coral Area
Exposed Reefs
Total area of exposed category recorded ~113 km2 from Andaman Islands
Spatio-temporal changes in the coral environs due to 2004 Sumatra Eq.

## Slide 53
Thank you